## Slide 1
August, 2015
Dining Set Sofa
TV Rack
Ripley Packaging Guideline

## Slide 2
Content
1. Preface P3
2. Specification for Shipping Carton P4 3 Packaging Guideline· P5
+ Table Packaging P6
+ Chair Packaging P13
+ KD Chair Packaging P17
+ Sofa Packaging P19
+ KD Sofa Packaging P21
+ TV Rack Packaging P23 4. Packaging Test P25
5. Shipping Carton Closer P26
6. Other Packaging Materials P27 7. Pallet Stacking and Pre-cautions P30
8. Container Loading and Pre-cautions P32

## Slide 3
1. Preface-Ripley packaging standard
The guideline contains general information for the packaging of RIPLEY products. A detailed specification for each project is defined. These sp- ecifications indicate the standard quality requirements of the packaging. All products purchased by RIPLEY must be packed in accordance with the requirements set out in this guideline. The products and packages must arr- ive at RIPLEY without damage. Vendors should strictly follow the stan- dard. Failure to meet these requirements may result in fines.
RIPLEY packaging standards is developed to:
Lower Defective Returns: Defective packaging significantly result in cus- tomer returns, and loss of customer confidence in our merchandise, which directly relates to our profitability and reputation.
Unified Application: The packaging guideline is able to support a unified package and standard for various materials of goods for RIPLEY to ac- hieve consistency and corporate image.
Environmental Impacts: The overall results of the guideline show a more material saving, green material using.

## Slide 4
Double Wall Corrugated Paper Board
2.Specification for Shipping Carton
Material of shipping carton is decided by the weight and shape of the produ- cts. All the shipping cartons are required to be made of double wall corruga- ted paperboard (AB flute/BC flute). With the standard Bursting strength 200 LBs/IN2. For bettrr carton quality, RIPLEY has the right to request higher spec.
Approximate Flute Height
A Flute
3/16" (4.7mm)
B A Flute
19/64" (7.5mm)
B Flute
7/64" (2.7mm)
C Flute
9/64" (3.6mm)
B C Flute
1/4" (6.4mm)

## Slide 5
3.Packaging Guideline
This section of the guideline gives the specifications to all RIPLEY ven- dors of the structure package. The standards of the packaging structure are designed to ensure the intact of the cargos during shipping and storage. In order to meet the standards, appropriate packaging material and right type of master carton should be applied. For RIPLEY furniture products, we are here to divide into several categories:
+ Table Packaging
+ Chair Packaging
+ KD Chair Packaging
+ Sofa Packaging
+ KD Sofa Packaging
+ TV Rack Packaging

## Slide 6
FTD Top Cover
EPS
FTD Bottom Cover
EPS Corner
EPE Film
EPS
Table Top Tool Kit
HDPE Bag
Manual
Table Leg HDPE Bag
EPS Corner
Table Packaging
Example 1. Table top + Table legs in one packaging
Note : EPS material around the product is compulsory. Standard specification: Density: 20kg/m3, Thickness: 15mm.

## Slide 7
Note: Density of EPS : 20kg/m3 Density of EPE : 30kg/m3
Table Packaging
Example 1. Table top + Table legs in one packaging
Shipping carton packaging
FTD. (Full-Telescope Design-Style Box): shipping carton of table and legs.
Inner cushioning packaging
EPS cushion: protect table top from dropping, transportation, knocking etc. The thickness of EPS is 15mm, EPS should be used while big gap existed between the table top and carton.
EPS corners / sheet: protect and strengthen the four angles and six surfac- es of the shipping carton.
EPE Film: cushion between table top and inner carton to prevent the abras- ion of table top surface.
For the table top into the carton, using 0.5mm EPE film to be the inner pac- kaging material.
HDPE Bag: pack the “Tool Kit” and table legs.

## Slide 8
Table Packaging
Example 1. Table top + Table legs in one packaging
Packaging style
FTD(Full-Telescope Design-Style Box)

## Slide 9
Table Packaging
Example 1. Table top + Table legs in one packaging
Style drawing
The drawing should include structure, dimension and other remarks.
Printing side is the side which can show information of products on the out- er carton.
The top cover is the printing side of FTD(Full-Telescope Design-Style Box)
Corrugated direction is decided by carton style and dimension. The width d- irection of carton is the corrugated direction of FTD(Full-Telescope Design- Style Box), marked as
TOP
RIGHT
LEFT
FRONT
XX XX XX BACK
XX
XX
XX
XX
Packaging information
XX
Vendor: XXXXXXXX Packing Format: XXXXXXXX Product Name: XXXXXXXX Scale: 100%
Description: XXXXXXXX Printed Side
Project related information
Various lines such as cut, crease and perf.
Main dimension should be marked.
Material: XXXXXXXX
Bursting Strength: XXXX(LBs/IN2) Edge Crush Test : XXXX(LBs/IN) Tolerance: ±XX INCHES
Size: 00(L) X 00(W) X 00(H) (INCHES)
Table Packaging
Corrugated direction

## Slide 10
Note : EPS material around the product is compulsory. Standard specification: Density: 20kg/m3, Thickness: 15mm.
6
Table Packaging
Example 2. Table top , Talbe legs into different
Table top packaging:
FTD Top Cover
FTD Bottom Cover
EPS Corner
EPE Film
Table top
HDPE Bag
Manual
EPS
Tool Kit
EPS Corner
EPS
Paper Cushion
10

## Slide 11
Note: EPS material around the product is compulsory. Standard specification: Density: 20kg/m3, Thickness: 15mm.
6
FTD Top Cover
FTD Bottom Cover
EPS
Table Legs EPE Film
EPS
Table Packaging
Example 2. Table top , Table legs into different Table legs packaging:

## Slide 12
Note: Density of EPS: 20kg/m3 Density of EPE: 30kg/m3
Table Packaging
Example 2. Table top , Table legs into different
Shipping carton packaging
FTD(Full-Telescope Design-Style Box): the shipping carton of table top and legs.
For the information of shipping carton style, please refer to page8--9.
Inner cushioning packaging
EPS Cushion: protect table top from dropping, transportation, knocking etc. The thickness of EPS is 15 mm, EPS should be used while big gap existed between the table top and carton.
EPS Corner/Sheet: protect and strengthen the four angles and six surfaces of the shipping carton.
EPE Film: the cushion between table top/ legs and inner carton to prevent the a- brasion.
HDPE Bag: pack the “Tool Kit”.

## Slide 13
Chair Packaging
Example . Chair packaging
1.Chair without arm.
HDPE Bag
Chair HDPE Bag
Manual
EPS Corner
RSC
Note: Two chairs need to be packed into one carton.
2.Chair with arms.
HDPE Bag
Manual Chair
EPS Corner
RSC
Note: One chair need to be packed into one carton.

## Slide 14
Chair Packaging
Example . Chair packaging
Shipping carton packaging
RSC(Regular Slotted Container): shipping carton of chair.
Inner cushioning packaging
“L” shape EPS Corner: strengthen the four angles of the outer carton. HDPE Bag: inner packaging of the leathery seat and the back of chair.
Note: Density of EPS: 20kg/m3

## Slide 15
Chair Packaging
Example . Chair packaging
Packaging style
RSC(Regular Slotted Container)

## Slide 16
Chair Packaging
Example . Chair packaging
Style drawing
FRONT
LEFT
BACK
RIGHT XX
TOP
BOTTOM
TOP
IN SIDE
IN SIDE
IN SIDE XX
IN SIDE XX
BOTTOM
Project related information
Various lines such as cut, crease and perf.
XX
Packaging information
Main dimension should be marked.
Vendor: XXXXXXXX Packing Format: XXXXXXXX Product Name: XXXXXXXX Scale: 100%
Description: XXXXXXXX Printed Side
Material: XXXXXXXX
Bursting Strength: XXXX(LBs/IN2) Edge Crush Test : XXXX(LBs/IN) Tolerance: ±XX INCHES
Size: 00(L) X 00(W) X 00(H) (INCHES)
XX
XX
XX
XX
XX
XX
Chair Packaging
Drawing should include structure, dimension and other remarks.
Printing side is the side which can show information of products on the out- er carton. IN SIDE can’t be used as the printing side. It only can be printed with contents which don’t need to be displayed.
Corrugated direction is decided by carton style and dimension. The height direction of carton is the corrugated direction of RSC(Regular Slotted Cont- ainer), marked as
Corrugated direction

## Slide 17
Front Leg Apron x4
HDPE Bag
EPE Film
Tool Kit
EPS Corner
Cushion Seat
EPE Film
HDPE Bag
EPE Film
HDPE Bag
HDPE Bag
Outer Carton
Chair Back
Manual
KD Chair Packaging
Example . Knockdown chair packaging
Note: Two chairs should be packed into one carton. Cushion seat should be packed in individual HDPE bag.

## Slide 18
KD Chair Packaging
Example . KD chair packaging
Shipping carton packaging
RSC(Regular Slotted Container): the shipping carton of knockdown chair. For the information of shipping carton style, please refer to page15--16.
Inner cushioning packaging
“L” shape EPS Corner: strengthen the four angles of the outer carton. EPE Film: the cushion between each layer to prevent the abrasion.
HDPE Bag: pack the “Tool Kit” and the accessories of knockdown chair.
Note: Density of EPS: 20kg/m3 Density of EPE: 30kg/m3

## Slide 19
Sofa
Corrugated Paper
Corrugated Paper
Manual
Corrugated Paper
FTD Bottom Cover
Sofa Packaging
Example . Sofa packaging
Corrugated Paper
EPE Film
EPS
HDPE Bag (T=0.03mm)
HDPE Bag
(T=0.1mm)
Add two piece of EPS into the FTD if the sofa feet are longer.

## Slide 20
Sofa Packaging
Example . Sofa packaging
Wrap the sofa with HDPE bag ( thickness: 0.03mm ) to avoid dust.
Use EPE film and corrugated paper to warp the edge and coner of the s- ofa in order to prevent it from the injury of impact and friction during moving.
Finally use HDPE bag(thickness: 0.1mm) to wrap the outermost of the s- ofa to fix the corrugated paper.
Note: Density of EPS: 20kg/m3 Density of EPE: 30kg/m3
The corrugated paper is AB flute. Bursting strength of the corrugated paper is 350 LBs/IN2. Edge crush test of the corrugated paper is 51 LBs/IN.
20

## Slide 21
KD Sofa Packaging
Example . KD Sofa packaging
Sofa Legs EPE Film
KD Sofa EPE Film Manual
HDPE (T=0.03mm)
RSC Carton
Corrugated Paper board

## Slide 22
KD Sofa Packaging
Example . Sofa packaging
Shipping carton packaging
RSC(Regular Slotted Container): the shipping carton of KD sofa.
For the information of shipping carton style, please refer to page15--16.
Inner cushioning packaging
Wrap the KD sofa with HDPE bag ( thickness: 0.03mm ) to avoid dust.
Use EPE film to warp the edge and coner of the KD sofa in order to prev- ent it from the injury of impact and friction during moving.
Use EPE film to wrap the KD sofa legs.
Use corrugated paper board to increase the strength of the outer carton.
Note: Density of EPE: 30kg/m3
The corrugated paper is AB flute. Bursting strength of the corrugated paper is 350 LBs/IN2. Edge crush test of the corrugated paper is 51 LBs/IN.

## Slide 23
TV Rack Packaging
Example . TV rack packaging
EPE Film
Manual Tool Kit
Leg
Accessory Box
HDPE Bag
EPE Film
TV Rack
Corrugated Paper Cushion
Corrugated Paper Cushion
Corrugated Paper Corner
Shipping Carton
ASSEMBLY INSTRUCTION

## Slide 24
TV Rack Packaging
Example . TV rack packaging
Shipping carton packaging
RSC(Regular Slotted Container): the shipping carton of TV rack.
For the information of shipping carton style, please refer to page15--16.
Inner cushioning packaging
“L”shape Corrugated Paper Corner: strengthen the four angles of the outer carton.
EPE Film: the cushion between each layer to prevent the abrasion. HDPE Bag: pack the “Tool Kit”.
Accessory Box: pack the five legs and Tool kit.
Note: Density of EPE: 30kg/m3

## Slide 25
Samples should be the untested actual package and product, but if one or both are not available, the substitutes shall be as identical possible to actu- al items. Packages that have already been subjected to the rigors of transp- ortation cannot be assumed to represent standard conditions. In order to i- nsure testing in perfect condition. Products and packages shipped to certifi- ed laboratories for testing must be:
Over-packaged for shipment to the laboratory or repackaged in new packa- ging at the laboratory.
The tests shall be performed on each test sample in the sequence indicate- d in the following table:
The test specification must conform to ISTA 2C.
6
4.Packaging Test
Sequence | Test Category | Test Type | Test Level | For ISTA Certification
1 | Atmospheric Preconditioning | Temperature and Humidity | Ambient | Required
2 | Atmospheric Conditioning | Controlled Temperature and Humidity | Temperatue and Humidity chosen from chart | Optional
3 | Vibration | Random Under Dynamic Load | Calculated Top Load differs for Distribution Channel, package size and configuration. Random vibration spectrum differs for Distribution Channel. | Required
4 | Shock (Alternative methods allowed-select one test type) | Drop | Height varies with packaged-product weight and Distribution Channel | Required
 |  | Exception One and Two Incline-Impact (Conbur) | Impact Velocity varies with packaged-product weight | 
 |  | Horizontal Impact | Impact Velocity varies with packaged-product weight | 

## Slide 26
5.Shipping Carton Closer
Tape sealing
All open edges to be tape sealed using opp tape(Diagrams show tape seali- ng required).
Full length of all outer seams securely sealed with strips not less than 2’’wi- de. Tape thickness must not be less than 2 mils.
Do not overﬁll a bulk carton as this can bulge, leading to instabillity in stack-
ing and subsequent failure in use etc.
Securely tape top and bottom ﬂaps of bulk cartons without obscuring the e- nd idetiﬁcation panel.
6

## Slide 27
Specification: width 11.5mm, thickness 0.8mm
For full telescope style box, banding is a must. When product is less than 1- 0KG, tape is suggested. More than 10KG, banding is suggested.
6
6.Other Packaging Materials
Banding
Material: PP
Banding must not cover information or graphics on label. Tension on bandi- ng must be tight enough to hold corrugated lid in place without damaging p- ackaging.
INCORRECT
CORRECT
Cartons are to be banded using plastic strapping only, jointing is to be by fr- iction weld (hot sealed).

## Slide 28
Corner post is made of multi-layers of recyclable cardboard paper bonded together and form an L shape. The thickness must be 5mm and the width A x B must be 50 x 50 mm.
Corner post must be used to protect the edges of the boxes and keep the products square on the pallet.
6
Corner post
Material: Recyclable cardboard paper
28

## Slide 29
Stretch wrap
Material: PE
Stretch wrap must be used as a cargo stabilizer. It should be made of Low- Density Polyethylene. Stretch wrapping can be applied by hand or by mac- hine.
While wrapping, it is suggested to start from bottom to top. Overlappping p- attern is required and the width of overlapping is recommended to keep 2-4 inches. Ensure bottom layer is double-wrapped.
6
Stretch Wrap
29

## Slide 30
Avoid
Best
c
7.Pallet Stacking and Pre-cautions
30
If stacking with pallets, make sure the protection of cargos, optimization st- acking should be calculated during handling and storage. Also, the conven- ience of shipping should be taken into consideration. (See illustrations bel- ow)
The result of interlock stacking is a 45% to 55% lossing compression stren- gth.
Interloc |  |  |  | k stacking |  |  | 
Colu |  | mnar sta |  |  | king | 

## Slide 31
Overhang is prohibited.
Damage will occur when master carton extends past the edge of the pallet.
If various packages can’t be avoided to stack together, heavier packages s- hould be placed on the bottom in order, shown as below:

## Slide 32
HANDLE WITH CARE
Calculate the reasonable loading method; provide the loading drawing b- efore loading container.
Check the outer package carefully before loading. Replace the outer pa- ckage if it is damaged.
Keep the weight balanced. The gravity should be in the centre of the co- ntainer that can avoid collapse during shipping and handling.
Methods which may damage the quality of products like throwing, tramp- le, clamping are forbidden during loading.
Cartons need to be stacked neatly and intercross stacking is not allowed during loading without pallets.
Heavier packages should be placed on the bottom while go with LCL.
The sequence of loading is row by row from inside to outside. Standing in the carton is not allowed.
To prevent collapse, vendors must check after loading and make sure c- argos are not too loose.
STACK ROW BY ROW FROM
DO NOT STAND ON THE CARTON INSIDE TO OUTSIDE
DO NOT THROW
8.Container Loading and Pre-cautions

## Slide 33
August, 2015
Dining Set Sofa
TV Rack
Ripley Packaging Guideline